GX-Ⅲ Type Multi-Purpose Electric Ion Operating Apparatus

This is a multi-purpose operating instrument, which has been widely adopted by many hospitals all over China such as the 1st Hospital Attached to Chengdu Huaxi University of Medical Science, the 1st Hospital Attached to Guangzhou Zhongshan University of Medical Science, the 2nd Hospital Attached to Zhejiang University of Medical Science, the People’s Hospital of Henan Province, the People’s Hospital of Heilongjiang Province, the People’s Hospital of Jiangsu Province, the People’s Hospital of Liaoning Province, the People’s Hospital of Hunan Province, Dermatology Prevention Hospital of Fuzhou City, Mother’s and Children’s Hygiene Hospital of Guangxi, Aesthetic Surgery Hospital of Technology and Industry for National Defense and etc. With high cure rate, desirable cure effect and good reliability, it is also easy to operate and hence sells very well in international market. Its working principle is: heated by plasma flame, the temperature between contactor and tissue will rise to about 3,000℃ instantly, which will then vaporize the tissue and the disease will thus be permanently killed with little damage to healthy tissues. Compared to CO2 Laser Machine, this instrument can also be applied to bloodless operation but with better performance, lower price (only its half), less failure, more service life and more broad application (can be applied to hospitals at all levels). It is an efficient clinical assistant.

Ⅰ. Features:

1. The operation begins with the metal contactor getting close to or being inserted into the body tissue. With the contactor, it is simple, convenient to operate with great accuracy. The apparatus can be used continuously or off and on by pedal switch.

2. The flame is adjustable to meet the requirements raised by different diseases. For long flame(can be used to coagulate), it features weak penetrating power, larger flame, bigger burned spot, stronger surface destructive power, better effect in hemostasia, and is therefore usually applied to operations that are prone to bleeding in Ophthalmology & Otorhinolaryngology and Gynecology. For short flame(can be used to cut), it features strong penetrating power, smaller flame and burned spot; it can destroy the inside of tissues and hence is usually applied to operations in which bleeding hardly appears in dermatology, surgery as well as tissue cutting and etc.

3. The out-put power is continuously adjustable. When the power is increased, it can vaporize and cut the tissue ; while the power is lowered, coagulation takes place.

4. The metal contactor is flexible which can be lengthened or bended as needed to meet different treatment depths and angles.

Ⅱ.Technical specification

1. Voltage: 220V±10％; Frequency: 50HZ

2. Power: 100VA

3. Volume: 14×32×32cm3

4. Weight: 6kg

Ⅲ. Application:

1. Dermatology department: fleck, pigmented nevus, flat wart, common wart, planar wart, eczema, hemorrhoidal vessels, nevus flammeus, telangiectasis, skin neoplasm, eyelid xanthoma, trichoepithelioma, verrucous nevus, sebaceous nevus, spiroma, syringoma, age pigment, congenital stain, hemorrhagic granuloma, cutaneous horn, bottle nose, removing tattoo, removing eyebrow tattoo, abscess, removing facial carrion, helosis, and recovering some kind of scar etc.

2. Surgery (rectum branch): hircismus, peritomize, anal fissure, anal fistula, perianal abscess, external hemorrhoid, rectal polyp, anal papilla, head lump, urethral caruncle and etc.

3. Stomatology department: gingival hyperplasia, epulis, bleeding gums, lichen planus, pericoronitis, dental ulcer, mouth cyst and etc.

4. Otolaryngology department: rhinopolypus, external ear tumor, chronic pharyngitis, tonsillitis, luette, tongue tie operation and etc.

5. Gynecology department: cervical erosion, cervical polyp, cyst of vagina and etc.

GX-ⅢB Type, GX-ⅢC Type, GX-ⅢD Type, GX-ⅢE Type Multi-Purpose Electric Ion Operating Apparatus

These four types are newly developed operating apparatus which not only combines all the functions of GX-Ⅲ Type but also increase the field- coagulating function. In other words, it is a combination of GX-Ⅲ Type Operating Apparatus and radio frequency therapy apparatus or microwave therapy apparatus. The newly-developed types are equipped with bipolar needle, bipolar forceps and bipolar clamps, and the alternating field produced between the two polar will vibrate the negative and positive ions as well as electric dipoles within the tissue, and hence in this way make them instantly heated to around 100℃. This process helps to whiten the diseased tissue and make it coaglated and shrunk into necrosis. All the treatment process entails no wound, fog or bleeding with little damage, and therefore meets the special requirements in treating diseased tissue in which blood vessel are crowded.

| Type | Application | Appendix |
| --- | --- | --- |
| GX-ⅢB Type It is usually applied in Stomatology & Otolaryngology | Besides the applications that GX-Ⅲ is capable of, it can also be applied to treating chronic hypertrophic rhinitis, chronic allergic rhinitis, nasopharyngeal cancers, hypertrophy of tonsil, chronic pharyngitis, hyperplasia in the lymphoid tissue, papillary epithelioma and all kinds of hemangioma etc. | Besides the equipments that GX-Ⅲ contains, it is also equipped with 2 short bipolar needles, 2 long bipolar needles and 1 bipolar forceps. |
| GX-ⅢC Type It is usually applied in Rectum. | Besides the application that GX-Ⅲ is capable of, it can also be applied to treating internal hemorrhoid, external hemorrhoid, mixed hemorrhoid, fibroma in the anal papilla, rectal polyp, some exterior lumps and neoplasm etc. | Besides the equipments that GX-Ⅲ contains, it is also equipped with 1 bipolar clamps, 1 bipolar round contactor and 1 circular-tube contactor. |
| GX-ⅢD Type It is usually applied to Gynecology. | Besides the application that GX-Ⅲ is capable of, it can also be applied to treating erosion of cervix, cervical polyp and etc. | Besides the equipments that GX-Ⅲ contains, it is also equipped with 1 bipolar round contactor, 1 circular-tube contactor and 1 bipolar forceps. |
| GX-ⅢE Type It is an integrated type of GX-Ⅲtype, GX-ⅢB type, GX-ⅢC type, and GX-ⅢD type. | The same as GX-Ⅲ, GX-ⅢB, GX-ⅢC, GX-ⅢD type | The same as GX-Ⅲ, GX-ⅢB,GX-ⅢC, GX-ⅢDtype |

Producer: Nanning Kelun New Technology Co., Ltd

Applied Physics Research Institute of Guangxi Academy of Science

Add: 6th floor Guangxi Academy of Sciences Building, No. 98 Daling Road, Nanning, Guangxi, China.

(You can take public bus No.4/58/62/76/207/222/604/605 and get off at the station of Crossroad of Daxue Road and Dalin Road, then turn on right and go straight about 400m.)

Tel: 0086-0771- 3213883

Fax: 0086-0771-2273929

Business Contact: Luo Siqiang(mobile phone: 13977181102 )

Zip code: 530003

Website: www.3213883.cn

E-mail: 562966638@qq.com